Hurricane Coming

and you don’t have much time?

# What to do to safeguard your house

## URGENT

For board houses not well

fastened to foundations,

bring indoors a water container

or other heavy objects to hold

house down

Trim branches of trees								that might fall. This will 								reduce the pressure on the 							tree from the wind

Board up windows to prevent

flying objects breaking them

and the damage this can lead

to

If you have more time………..

Add extra nails and a cover strip							to overhangs particularly at 							gable ends

Put in more nails or screws

along the edge of the roof

to stop lifting

Fit one hurricane strap or								clip on each rafter if they 								are missing

Fit Collar Ties between every

other pair of rafters to hold

together the two sides of the

roof