| Drill | D4-04 |
| --- | --- |
| Category | Emergency Response |
| Type | Contingencies |
| Subject | Power failure |
| Security Level | 1 or 2 |

## INTRODUCTION

- The continuity of power supply is an important factor in security arrangements for any port facility. Where municipal supplies can be unreliable at times, most port facilities will have back-up power arrangements for their essential services. It is important that security equipment and services are included as essential services to be supplied by back-up power. Nevertheless, plans should be in place to ensure the continuation of security services.

## AIM

- To enhance the proficiency of port facility staff in responding to a power failure.

## OBJECTIVES

- Operations staff to switch on backup power within the time limit as specified in the PFSP

- Security staff to respond to power failure according to procedure in the PFSP.

## DESIRED OUTCOMES

- On completion of the drill, port facility staff will be able to:

- Switch on backup power quickly in the event of a main power failure.

- Respond appropriately to a power failure.

## RESOURCES

Personnel

- Control Team

- Chief Controller – This can be the PFSO

- Chief Electrical Engineer

- Duty Electrical Technician.  Additional staff may be needed

- Players

- Port facility operations staff

- Port facility security staff.

- Safety Officer – The appointment of a safety officer for this drill should be considered due to the fact that part of the port facility will be operating in darkness.

Material

- The Chief Controller will make arrangements with the chief electrical engineer in the Port Facility for power failure to occur at selected zone in the Port Facility to facilitate the conduct of this drill. Should the Port Facility have the resources to provide emergency power for all security services in addition to port facility operations, consideration should be given to simulate a breakdown of the emergency power arrangements as well as the municipal power.

- Communication

- For players – The existing communication infrastructure will be used.

- For Controllers – Mobile phone as preferred means with walkie-talkie as back up.

- Others

- Refreshment or meals – if required

- Room for briefing and debriefing with computer, projector, screen and chairs

- Stationery for note taking

Budget

- Funding may be needed for the following:

- Refreshments for debrief.

- Reimbursement of expenses incurred by controllers or staff, if any.

## SCHEDULE OF EVENTS

- Refer to Drill Announcement (or if there are changes, an updated Schedule can be posted here)

## SCENARIO

- The aging electrical infrastructure in the region coupled with the recent increase in electrical demand has lead to several blackouts in recent times.  While the port facility has its own emergency power supply, it may take time for the emergency power supply to become available.  Security staff has to be prepared to take additional measures to ensure the security of the port facility is not compromised while electrical supply is not available.

## TASKS

- For Controllers:

  - This drill will involve switching off the security lighting and should be conducted at night.  Where a Port Facility operates round-the-clock, the drill may be confined to a selected zone where both the main and emergency power supply could be isolated and switched off to achieve the desired effect of no security lighting.

  - At the appointed time, the duty electrical technician will isolate the emergency power to the selected area and then switch off the main power supply for the security lighting.

  - After completion of the drill, the main and emergency power supply must be restored and tested to be working.

  - The Chief Controller will conduct the drill in accordance with the events listed in the Master Events List.

  - The Chief Controller should position himself at a suitable location to discreetly observe the proceedings.

  - The Safety Officer should follow the security staff as they carry the drills and especially when part of the port facility is in darkness.

- For Players.  This drill will require Port Facility security staff to respond to a power failure that affected the security lighting of a certain portion of the port facility.  The security staff is expected to respond to the power failure and adopt the necessary measures.

## MASTER EVENTS LIST

The timing of the drill is not critical. Expected response column is just a guide and should be substituted with existing standard operating procedure of port facility.

| S/N | Time | Event | From | To | Means of Delivery | Expected Response | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Date: | DD/MM/YYYY |
| 001 | 1930 | All participants in position |  |  |  |  |  |
| 002 | 1935 | Drill commence | Chief Controller | All participants | Walkie Talkie | None | “Drill Start” |
| 003 | 1955 | Security lighting failed | Controller | Security staff | Physically cut off power | Inform ops department, take actions to maintain security |  |
| 004 | 2100 | Drill completed | Chief Controller | All participants | Walkie Talkie | Dispersal of personnel/ equipment | “Drill End” |
| 005 | 2101 | Restore main and emergency power supply | Chief Controller | All participants | Restore all services |  | Power supply must be tested to be fully functional |
| 006 | 2130 | Hot Wash | Chief Controller | All participants |  | N/A |  |

## TERMINATION

- The drill may be terminated under any one of the following conditions:

  - When security staff have completed deployment in response to power failure.

OR

  - At a pre-determined time after the start of the drill.

OR

  - Upon the Chief Controller’s instruction.