# Dominica

Sustainable Energy Plan

## Draft

November 14, 2002

# Background

Dominica is known as "The Nature Island of the Caribbean" due to its abundant plant and animal life, extensive park system, volcanic peaks, lava craters, waterfalls, rivers, and lakes.  It is blessed with abundant resources and significant potential for economic and social development.  Dominica’s population of approximately 75,000 inhabits the island covering 746 square kilometres, resulting in one of the lowest population densities in the region.  Despite its natural beauty and abundant green spaces, Dominica faces significant challenges regarding it development.  Its economy is predominantly agriculturally based, with a high level of dependence on bananas.  Given recent difficulties with the Caribbean banana market and tourism industry, Dominica’s economy has suffered.

In order to drive sustainable economic development, Dominica requires reliable and cost-effective types of infrastructure.  Among the various sectors, electricity and transport represent considerable challenges for Dominica.  The relative small size of the system and the absence of domestic petroleum resources have resulted in high cost electricity and gasoline rates.  Further, the reliability and efficiency of the current electric system and public transportation is extremely limited.  However, Dominica possesses considerable natural resources to provide for its energy needs with a combination of renewable energy technologies – hydro, wind, biomass, geothermal, and solar – and increased energy efficiency.  It, given its small physical size and population also has potential to serve as a model or pilot country for electric/hybrid vehicles and public transportation systems.

As Dominica works to further develop its tourism sector, particularly focused on eco-tourism, the use of clean renewable energy end energy efficiency technologies will enhance this sector.  These technologies will also serve great benefit to the agricultural, industrial, commercial, governmental and residential sectors, since energy use impacts all aspects of life.  Dominica’s Medium Term Economic Strategy Paper 2000-2001 states that major investments in electricity generation and distribution are necessary to facilitate the requirements for the further diversification of the economy.  Additionally, with growing concerns over the global environment, including greenhouse gas emissions, Dominica may demonstrate the viability of sustainable energy systems to other nations.

Currently, diesel generators fuelled by imported oil and hydropower plants generate Dominica’s electric power.  There are two operating diesel plants (Fond Cole and Portsmouth) and three hydropower facilities (Laudat, Trafalgar and Padu).  There have been no new investments in hydropower generation in over 10 years, while thermal generation has grown modestly.

Electricity rates in Dominica have risen significantly in recent years (see Figure XX). At present, residential customers are paying EC$0.57/kWh (US$0.21) for the first 50kWh and EC$0.662/kWh (US$0.244) for additional kWh.  Additionally, fuel surcharge is calculated monthly and added as a per cost to the total consumption.  The fuel surcharge in May was EC$0.0516 (US$0.0189) per kWh.   This is among the highest tariffs in the Eastern Caribbean and is currently the source of concern and protest among many residents.

Additionally, the contraction of the economy and negative growth in the population has resulted in a very slow growth in peak electricity demand over the past few years (See Figure 1).  While much of the generating capacity is old and will need to be replaced or retrofitted in the coming years and future growth in demand is expected, there is not significant interest in additional investments in generating capacity at this time, principally due to limited capital available.

The customer base for electricity services comprises domestic, commercial, hotel, industrial, lighting and street lighting.  Figure 2 illustrates the proportions of consumption according to the major users.  Nationwide, electricity is provided exclusively by the Dominica Energy Services Ltd. (DOMLEC), which is owned by the Commonwealth Development Corporation (CDC).  According to the Electricity Supply Act of 1996, DOMLEC holds the sole and exclusive licence for electricity generation, transmission, distribution, and sale.

The transportation sector is a serious concern for Dominica in terms of sustainable energy use.  Currently, very limited statistics are available, but concern has been raised regarding unregulated bus routes and a proliferation of low-efficiency used car imports.

Dominica currently has no national energy policy or law, or renewable energy policy or statement, although an integrated plan for development is currently in the works and will include energy aspects.  The lack of an energy plan is viewed as a significant impediment to development of the country’s renewable energy resources and energy efficient programs.  Accordingly, this document builds upon the suggestion of the Integrated Development Plan and is a first step in overcoming this barrier.

# Goals of the Sustainable Energy Plan

The Sustainable Energy Plan lays out a strategy by which the energy production and use in Dominica may be transformed, becoming more economically and environmentally sustainable:

- Ensure the existence of adequate energy supplies at affordable rates to sustain economic development, while meeting current and projected power demand.

- Provide for stable, reliable, and affordable electricity supplies for all customers.

- Lower the price of electricity for consumers.

- Enhance the security of energy supply and use for all sectors of the economy.

- Allow reasonable incomes for businesses engaged in the local energy sector, while attracting international investment where appropriate.

- Promote energy efficiency and conservation at all levels of the economy in order to achieve optimum economic use of renewable and non-renewable sources of energy.

- Protect the local and global environment by maximizing the use of renewable-energy and energy-efficiency alternatives where viable.  This is especially relevant in Dominica as much of the renewable energy generation may take place in nature preserves.  It is essential that this be done in a manner that does not threaten biodiversity, forestation levels, and other environmental aspects.

- Promote the generation of income through energy exports produced from indigenous energy sources (esp. geothermal resources).

# Energy Sector Baseline

The following baseline is based on analysis provided by the Dominica Electricity Services Ltd. (see Table 1: Operating Statistics in Dominica, 1996-2001).  The baseline has been established for purpose of comparison and is consistent with the goal of ensuring that sufficient, cost-effective, and reliable electrical power will be available to all customers in keeping with expected annual economic growth rate.

In the early 1950’s and 1960’s, hydropower met approximately 90% of electricity generation requirements in Dominica. In 1994, Dominica generated 78% of its electricity from hydropower and 22% from diesel-powered plants.  Seven years later, hydropower dropped to 33% and diesel accounted for 76%.  This has been changing over time, due to weather trends (rainfall levels), increased demand, and more use of diesel-powered generators.  It is resulting in increased dependence on imported fossil fuels and a variety of environmental impacts.

In terms of electricity sales, from 1994 to 2000, electricity sales increased by approximately 46.5% from 42,343 to 62,005 KWh x1000.  The sectoral distribution of sales remained very similar during the period with the Domestic sector accounting for 49% and 50% of the sales in 1994 and 2000 respectively.  This trend is expected to continue under a Business as Usual scenario due to an increase in demand in the Domestic sector, once Government implements its plans for electrifying the rural areas that are currently without electricity and new private housing development programmes are completed.  The 1991 Census reported that 76% of the population has electricity; as a result of rural electrification initiatives nationwide, this number has risen to approximately upper 90%.

In 2001:

- Installed capacity was 20.4 MW (Diesel = 12.8 MW; Hydro =  7.6), 37% renewable.

- Peak demand was 13.86 MW(66.7% of the load factor).

- One third of electricity was supplied by hydropower (27,036 MWh) and two-thirds by diesel (53,929 MWh).  The amount supplied by hydropower in 2002 is expected to increase, due to heavy rainfall.

- DOMLEC used 3,099,157 I.G.s of fossil fuel, at a cost of EC$10,678,000.

- Approximately 97% of the population is able to access the electrical grid.

# Sustainable Energy Plan: Energy Sector Scenarios

#### ELECTRICITY SECTOR TARGETS

This plan sets two specific targets for the electricity sector in Dominica for the year 2008 (5 years after the ratification of this plan by Cabinet): peak demand and renewable energy installed.

- Target Peak Demand: 13.86 MW, 0% change

- Target Renewable Energy Installed (% of total installed capacity): 12.6 MW (48% of total)

Dominica will maintain its peak demand at 13.86 MW.  The base assumption is that demand will naturally increase during this five-year period as a result of economic growth.  A series of energy efficiency measures highlighted in the subsequent section on required actions will serve to maintain the peak demand at 2002 levels.

The second target addresses the target renewable energy installed.  Due to the current shortage of installed capacity resulting in blackouts, DOMLEC is proposing the immediate installation of an Ormrod 3 MW heavy-fuel generator.  Taking this into consideration, in order to achieve 48% of the total installed capacity being supplied by renewable energy, a 5 MW of electricity generated by renewable energy must be added to the grid.  A potential scenario might be:

Currently installed

11 MW Diesel (41%)

7.6 MW Hydro (29%)

Projected installations

3 MW Heavy Fuel (11%)

5 MW Renewable Energy – wind, solar, biomass, or geothermal (19%)

# Sustainable Energy Plan: Required Actions for Achieving Targets

Attaining the foregoing targets is considered feasible, according to the information obtained by the Government of Dominica for the development of this Sustainable Energy Plan.  However, the present policy and regulatory framework requires adaptation to put in place suitable market rules and signals. Recommended actions for creating such an environment in which sustainable energy actions are implemented are described below.

##### Assessment of Market Potential

To expand the use of renewable-energy and energy-efficiency measures, it will be critical to ascertain, at least in broad terms, where key project opportunities exist.

In the case of renewable energy projects, one of the main prerequisites to attracting potential investors is a basic set of data identifying key resource locations and describing the likely quantity and quality of such resources.  A broad assessment of renewable energy resources, including wind, biomass, solar, and geothermal, will be assembled.  In some cases, such as geothermal energy, resource assessments have been undertaken for several years but have not resulted in the commercial development of a project.  As part of this Sustainable Energy Plan, additional site-specific assessments will continue in anticipation of locating quality resources with the potential for commercial exploitation.  In the area of wind-resource assessments, both broad national wind mapping and site-specific monitoring will be undertaken.

Action:  Compile renewable-energy resources assessments for wind, biomass, geothermal, hydro, and solar energy and conduct assessments where needed. Organize these into a single Renewable Energy Resource Database for use in promoting Dominica as a possible destination for renewable-energy investments, research and development, and export of energy.

Similar analyses of technical potential are also required for the energy-efficiency market.  It is assumed that opportunities for electricity savings, through conservation, the use of high efficiency technologies, and better management of demand, are plentiful.

Action:  An analysis/survey of the market potential for energy efficiency measures will also be undertaken.  This will review generation and consumption patterns throughout the country and in each of the key sectors.  These analyses will be used in the design of appropriate energy-efficiency measures and in efforts to attract entrepreneurial initiatives focused on energy savings.

##### Grid-Tied Renewable Energy Initiatives

- Electricity Generation Mix:  The current generation profile for Dominica consists entirely of hydro and diesel-powered generators.  The imported petroleum products make Dominica susceptible to swings in the international oil market.  The use of fossil-fuel generators damages the environment (loss of biodiversity, increased greenhouse gases, deforestation, erosion, etc.).  Further development of micro-hydro and new development of solar, wind, biomass, and geothermal projects would result in a positive impact on the national economy and the environment and ensure domestic energy security, as well as research and development into ocean thermal technologies.

Dominica has determined that it is in its best interest to add more renewable energy to its generation portfolio; accordingly the government will mandate the addition of such capacity in the national system.  This is a practice followed in various countries, including the UK’s Non-Fossil Fuel Obligation and the Renewables Portfolio Standard in several U.S.A. states.  Such a strategy may dictate that the utility must have available (or must deliver) a specific percentage of its electricity capacity via renewable-energy systems.  The mandated portion may increase over time to let the utility gain experience with them gradually.

Action:  Establish a Renewable Energy Portfolio Standard (RPS) for Dominica.  The RPS will impose that an additional 13% installed capacity be renewables-based by the year 2005 and 28% by the year 2010. The government will also adopt and enforce include regulations for the implementation and monitoring of this policy.  The policy must ensure that the renewable energy technologies used are cost-competive so that no price increase is passed on to consumers.

Dominica is blessed with abundant geothermal resources, which provide the nation with tremendous economic opportunities.  Studies dating back to 1969 conclude that Dominica has excellent potential to generate power using natural steam.  It is believed that fully developed geothermal fields in Dominica could provide electric power generation anywhere up to 300 MW.  The two principal geothermal sites and their potential supply are Soufriere (25 MW), and Wotten (5 MW).  They can be harnessed to supply electricity services both to the domestic population and to international markets.  The Government of France is considering the construction of energy transmission lines between Martinique and Guadeloupe.  Given Dominica’s location between these two islands, it is falls squarely in the middle of any proposed transmission line.  It could produce geothermal power and sell it to both islands.

Action:  Review geothermal assessment reports to date and conduct up-to-date analysis.  Assess the feasibility of supply of electricity to Martinique and Guadeloupe.  Assess domestic generation of electricity based using geothermal resources.

Given its prime location and its geography, Dominica possesses ideal wind energy conditions for the use of wind turbines.  Analysis indicates that wind energy could significantly lower the price of electricity for consumers and benefit the national economy and the environment.

Action:  Conduct a further assessment of wind energy resources.  Based on the assessment develop a medium scale wind farm that connects to the grid.  Utilize wind turbines, when appropriate, for remote applications.

- Adopt Policies that Encourage Private Power Development: Achieving specific renewable-energy targets in Dominica might not occur under the current exclusive arrangements currently afforded to Dominica Electricity Services Ltd.  In many cases independent power producers with experience in renewable energy would be better suited to develop these projects.  Therefore, policies and regulations that permit and encourage Independent Power Producers (IPPs) will be developed.  These regulations will describe the potential relationships between the IPP and the utility, which might include model power purchase arrangements, under which the third-party power developer sold electricity to the utility or, alternatively, wheeled power on the utility lines to specific consumers (such as a hotel).

Action:  The Government of Dominica will explore alternatives to the current electricity monopoly granted to Dominica Electricity Services Ltd., including consideration of provisions that make possible independent power projects that sell electricity to the utility.

- Renewable-Energy Capacity and Awareness-Building Initiatives: Among the greatest impediments to the widespread use of renewable-energy technologies is the limited capacity of key decision makers and technicians. In addition, utility officials and engineers lack the information necessary to select, develop, and use renewables within their system.  Likewise, gaining technical capacity in the operation and maintenance of renewable technologies would make it much more likely that the systems installed would be successful and achieved their full potential.

Action:  Establish a comprehensive renewable energy training initiative with the purpose of increasing the capacity to develop and utilize these systems among the utility staff and potential project developers.  This effort will be conducted in cooperation with CARILEC. The Government will request financial and technical assistance for it, from such sources as the Caribbean Renewable Energy Development Project (CREDP), in which it is a participating country.

The Government has determined that it is in the country’s best interest to catalyse the use of sustainable energy technologies, including renewables.  The policies and regulations resulting from this Plan will contribute to the accomplishment of this objective; however, the long-term success of such efforts depends on a high level of support from the general public.  A well-designed awareness and promotion campaign would result in a population that not only was more receptive to assuming the initial risks of these alternatives, but also would demand the incorporation of cleaner energy systems.

Action:  Initiate a national renewable energy education and awareness programme aimed at all sectors of civil society, to communicate the overall goals of the government with respect to the country’s economic development, protection of the environment, and the advantages of renewables.

- Establish Renewable-Energy Feasibility and Project Investment Fund: It is recognized that the initial cost of investment in renewable-energy facilities, coupled with the perceived risks of their use, may make it difficult for project developers to attract financing.  This situation often presents itself in the preparatory phases of the potential project (i.e., pre-feasibility and feasibility studies), but may also include project financing for well-designed, commercially viable projects.  Thus, it is critical to make funds available for investment in sound renewable-energy project opportunities.  While such funds would not account for the entire investment of any project, they would be targeted at catalysing additional resources and serving as seed capital for worthy ventures.

Action: The Government of Dominica will take the lead role in the creation of a dedicated renewable energy fund.  This fund will provide concessional financing for renewable energy project feasibility studies and for project investment.  The Government of Dominica will seek funds from several institutions, including the CREDP, the World Bank’s Prototype Carbon Fund, and international investors and donors to catalyse this financing.

- Establish Policies to Encourage and Enable Auto-Generation and Co-Generation: Under the current Electricity Act, Dominica Electricity Services Ltd. is the only electricity provider permitted within the national grid framework.  A commercial or industrial property is unable to generate its own electricity, with the exception of a few customers that were “grandfathered” in at the adoption of the policy.

Action:  The Government of Dominica will consider the establishment of policies that permit companies to generate their own electricity while still maintaining continuous link to the power grid.  This policy may also include a mechanism that permits auto-generators to sell excess capacity back to the utility.

- Establish Comprehensive Renewable Energy Regulations: In the absence of comprehensive power-sector reform, specific regulations will be required to govern areas such as independent power generation and the pricing and use of renewable-energy technologies.  Also, an independent regulator with enforcement powers will be required for their implementation.

Action:  Electricity regulations and an independent regulator governing the generation and use of private power, and specifically renewable-energy technologies, will be established.

##### Independent Renewable Energy Initiatives

- Create a National Solar Water Heating Initiative:  The abundant direct solar radiation in Dominica offers tremendous potential for solar-based water-heating applications.  It is estimated that the sun provides about 6 KWh of energy every day for every square meter of land.  Solar water heaters have proved technically viable and economically efficient in other Caribbean island nations.  Currently there is one company on the island manufacturing and selling solar water heaters, but there has been no formal public awareness campaign or promotion of the technology.  Given the high cost of electricity, and the significant load required for water heating, which show the cost-effectiveness and relatively quick return on investment required for solar water heating systems, the potential for a national awareness and promotion initiative is considerable.

Action:  Establish national solar water heating awareness initiative to target both the residential and the commercial sectors.  This initiative will be linked to the energy efficiency activities described below.

- Assess the Potential of Widespread Solar Photovoltaic Systems Installations: Solar Photovoltaic (PV) systems offer advantages for a diverse set of applications.  With its price falling and the cost of traditional electricity in Dominica remaining high, increasing PV may be a cost-effective alternative in several areas.  The assessment of PV in various applications will serve as a first step to eventual widespread use of PV systems.

Action:  Assess the potential and cost-effectiveness of solar PV systems for a variety of applications, both connected and unconnected to the grid.  Such applications may include back-up power for hurricane shelters and schools, demonstration units at gasoline service stations, and demonstration units at government buildings.

##### Energy Efficiency Initiatives

- Conduct a Comprehensive Energy End Use Analysis:  As a means of determining the energy use patterns of the various sectors of the economy a comprehensive study will be undertaken.  The results of this analysis will provide the necessary information regarding potential areas for energy efficiency applications and will serve to guide the other activities described in this Plan.

Action:  A study of energy end use practices in all sectors (public, commercial, residential, etc.) of the economy will be conducted in collaboration with DOMLEC.  This report will highlight key opportunities for energy savings.

- Initiate a Comprehensive Capacity-Building Initiative Among Personnel of Utilities Commercial Energy Plants, and Other Relevant Organizations:  A critical first step toward the success of any energy-efficiency initiative involves the development of appropriate awareness and technical capacity among the organizations and individuals that will participate in these programs.  Traditional utilities and other energy-sector personnel are often hesitant to promote strategies that effectively reduce the demand for electricity.  However, it has been well demonstrated that there are many business opportunities for both the utility and third party organizations that may result in attractive investments.  Further, the most cost-effective reductions in environmental impacts from the energy sector are typically derived from efficiency improvements.  There are many areas of training that will be useful in laying the foundation for a solid energy-efficiency program in Dominica. Such measures should address wide-ranging areas as business development and creative strategies to technical aspects of energy efficiency.  This initiative will seek to build a consensus among both existing electricity-sector personnel and potential entrepreneurs.

Action:  Implement a comprehensive energy-efficiency training program for utility personnel, hotel developers and engineers, potential entrepreneurs, and other relevant persons.

- Support and Assist in the Establishment of Energy Service Companies (ESCOs):  ESCOs are businesses that derive their income by generating energy savings for their clients.  They may be affiliated with the utility or operate as independent, third party enterprises.  They typically provide services for commercial businesses, such as the hotel industry.  It is common for them to enter into a contract with a client, such as a hotel, whereby they identify and help to implement opportunities to generate energy savings by retrofitting energy-consuming technologies and changing patterns of electricity consumption.  The ESCO receives payment for the consulting and engineering services it provides, which are typically less than the overall savings accruing to the client.  Thus, it is a win-win relationship for both. Significant energy savings might be realized via the government sector, industry, tourism and other commercial buildings.

Action:  Catalyse the creation of one or more ESCOs in Dominica.  The Government, in cooperation with an energy-sector venture capital fund (E&Co.), will assess the potential and seek opportunities to invest in one or more entrepreneurial enterprises.

- Launch a National Demand-Side Management (DSM) Initiative Designed to Reduce Residential Energy Consumption:  Residential energy consumption patterns in Dominica offer the potential for DSM measures to reduce electricity demand.  Effective DSM programs require well-designed and targeted campaigns that communicate to the population the need for and potential benefits from reducing consumption.  They often include printed materials describing successful applications of energy efficiency measures and the economic savings realized (newspaper advertisements or articles, brochures, and utility-sponsored seminars).  Promote building standards and codes both at the construction stages and throughout the life of buildings and infrastructure.

Action:   Dominica will implement a residential demand-side management (DSM) program intended to reduce consumption in the residential sector by 10% by the year 2010.

Action:     Dominica will establish regulations setting energy-efficiency standards and economic incentives for new construction.

- Support the Establishment of and Participate in the Caribbean Energy Efficiency Development Project (UNDP/GEF, PDF Block B):  A regional project for the promotion of energy efficiency is being prepared for implementation by the United Nations Development Programme (UNDP) with funding from the Global Environment Facility (GEF).  This project will assist participating countries in the identification and execution of energy-efficiency programs.  This project has the potential to offer Dominica technical and financial resources for its energy-efficiency activities.

Action:  Participate as an active member country of the newly launched Caribbean Energy Efficiency Development Project.

- Establish Guidelines for Energy Efficient Practices in all Government Buildings:  By establishing standards for energy efficient practices in all government buildings, two important objectives may be achieved.  First, given the considerable number of government installations, reducing energy consumption in this sector will contribute to the national efficiency goals and reduce costs.   Secondly, the Government will serve as an example to other sectors in the economy by adopting energy efficiency practices.  The Government may implement a variety of energy efficiency practices, including the use of energy efficient lighting and other appliances, training and implementation of energy conservation practices, and design and acquisition of efficient buildings for all new locations.

Action:  Assess the potential for energy efficiency practices in all Government buildings.  Based on this assessment, develop a standards manual for use by all government agencies describing recommended and/or required practices for existing and new buildings and equipment.

##### Transport Sector

Transport in Dominica is one of the main fossil-fuel-consuming sectors.  This situation is aggregated by the lack of an organized public transportation system, which is reflected in part by increased vehicle registration over the years.   The sector is also the source of a number of greenhouse gases, including principally, carbon dioxide (CO2), methane (CH4), and nitrous oxide (N20).  Dominica’s Greenhouse Gas Inventory has shown that the major GHG’s emissions are generated by the transport sector (50% CO2), energy industries (26% CO2), and commercial and industrial Uses (10% CO2).   Efforts to reduce GHG emissions will therefore be targeted at the three (3) main sources i.e. the transport sector, the energy sector and the commercial and industrial sector.

The global transportation sector is estimated by the International Energy Agency (IEA) to have been responsible for about 25% of world primary energy use and 20-25% of global emissions in 1990.  The current transport sector in Dominica comprises of vehicles used by private individuals and by commercial entities.  The private ownership sector is the least flexible to changes, because it is heavily dependent on petroleum-based fuels, and entrenched lifestyles.  Emissions from these sources could be expected to increase over time under a Business as Usual scenario, as the population increases and the economy continues to grow.

The Town and Country Planning Act covers all types of development and authorizes the formulation of a national development plan that is expected to provide a coherent and comprehensive land use policy that assesses special development needs.   This provides opportunities for the development of a sustainable transportation plan as part of the integrated development plan, which would link the various sectors within society.  For example, the road paving industry (asphalt) is one of the main emitters of non- CO2 gases in the form of non-methane volatile organic compound (NMVOC); thus this must be considered when decisions are made about the transportation infrastructure.

The monetary benefits to the economy and the individual of importing used vehicles as opposed to new vehicles is clear, but in terms of the environmental impacts, the increase in used vehicles within the mix of imported vehicles is not very beneficial. Relative to new vehicles, use vehicles may:

- Use more fuel than newer ones;

- Have defective emission control devices or none at all, and

- Have air conditioning units that still rely on ozone-depleting substances currently being phased out under the Montreal Protocol.

It must be noted, in connection with implementing international conventions for safeguarding the environment, that Dominica has no scientific methods in place to measure the potential impact of these used automobiles on the island.

The vehicle registration statistics available from the police department indicate that there are 12,900 vehicles registered.  Given the historical trends this number is expected to increase exponentially over the years, especially if the lack of a public transportation system is not addressed.

The marine-transport sector is similar to that of the other Caribbean islands, consisting of inter-island ferries, pleasure boats, cruise vessels, water sports craft, etc.  In 2000 the Government established a Maritime Administration and is now actively undertaking efforts to regulate that sector.

##### Transportation Sector Recommendations

The options for reduction of emissions from this sector will be developed in the context of a comprehensive transportation plan for Dominica, both to better regularize and minimize traffic flow and consequently reduce the emission of greenhouse gases. Many of the recommendations come directly from the Dominica’s National Communication prepared for the United Nations Framework Convention on Climate Change.  The main goal of the Transportation Sustainable Plan is to provide a reliable and efficient public transportation system in Dominica while diminishing the impacts of current mobilization means to the environment and the global climate changes.

1.	Establish regulations to provide incentives for the purchase and use of higher-efficiency vehicles and disincentives for less-efficient vehicles:  Since fuel economy has an inverse impact on emissions, it is necessary to address the increase in the importation of used vehicles.  The import regulations should restrict age, emissions, etc.  Tax and other incentives and disincentives can be used to promote the importation of newer vehicles for replacement.

Action:  Review current regulations and procedures to analyse the suitability of vehicles to be imported into the country.  Create new regulations and legislation where there are gaps.  With regard to marine transport, efforts should be made to include environmental-impact assessments and protection measures in the current control mechanisms.

Action: Restrictions on the importation of older foreign used vehicles. Ideally, the first approach to controlling or reducing CO2 emissions from exhausts pipes is to restrict the age of the vehicles on the roads to those that meet better emission standards. Consequent with this approach, will be the reduction in consumption of fuel, since older cars are generally less fuel-efficient than new cars.

Action: Legislation of fuel economy standards, including compulsory fitting of speed limiters.

Action: The mandatory installation of pollution removal devices such as catalytic converters in vehicular exhaust emission systems and the implementation of tougher legislation relating to exhaust emissions.

Action: Energy use efficiency improvements through the use of less carbon emitting fuels, such as natural gas, as well as unleaded fuel.).

- Steps must be taken to assess the current fleet of vehicles on the island, with a view to lessening their environmental impacts.  Currently no emissions testing is done in Dominica; vehicle registration consists merely of a visual and mechanical inspection by a licensing officer.

Action:  At least one emissions testing facility should be installed on the island.  In addition, statistical information must be collected on the environmental impact of the transport sector.

- Improve the public transportation system.  Addressing the lack of an organized and reliable public transportation system will not only serve to lessen the huge reliance on private vehicles for mobility, but will also have a positive impact on economic activity between communities.  Environmentally, decreasing in the number of privately owned vehicles on the road will reduce fossil-fuel consumption, greenhouse-gas emissions, and traffic congestion.  With a limited road network and increasing traffic congestion, and possibly increased private commuting cost in terms of fuel consumption and parking fees, a reliable public transportation system is potentially an excellent alternative.

Action:  Review the current legislative and other arrangements for public-transportation management, regulation, and monitoring.  Prepare a master plan to include route evaluations, costs, efficiency, parking fees, etc.  Limit the flow of traffic within city limits, and ensure whatever measures adopted are enforced.

- Database Development.  The ability to obtain support (both locally and internationally), for the measures undertaken will depend in the long run, on the ability to prove that the measures actually make a difference.  This can only be achieved by collecting and analysing data and building public awareness.  The ready availability of data will also make it much easier to plan and manage the transportation sector.

Action:  Establish a comprehensive database on the transportation sector to include information on marine transport.

###### Conclusion – Benefits to the Nation and the World

Dominica’s Sustainable Energy Plan will contribute significant benefits to the nation.  Additionally, the country will effectively demonstrate the feasibility and advantages derived from sustainable energy policies to a global audience.

The benefits of sustainable energy development in the case of Dominica are substantial, as the use of fossil fuel contributes to global climate change, local environmental damage, and growing debt due to significant foreign reserves being spent on fuel imports.  An indigenous fuel source and a sustainable-energy policy will bring about both environmental and economic benefits.  Additionally, the plan can benefit the land use policies and planning strategies undertaken in order to preserve the natural resources and control the potential negative impacts of future development.

Figure 1: Peak Demand and Growth in Demand

Source: Dominica Electricity Services Ltd., Annual Operational Statistics.

Source: Dominica Electricity Services Ltd., Annual Operational Statistics.

Source: Dominica Electricity Services Ltd., Annual Operational Statistics.

| Table 1: Operating Statistics in Dominica, 1996-2001 |
| --- |
|  | 2001 | 2000 | 1999 | 1998 | 1997 | 1996 |
| Sales of Electricity by Sector (KWh X 1000) |
| - Domestic | 31,772 | 30,872 | 30,023 | 28,716 | 26,721 | 24,698 |
| - Commercial | 17,068 | 16,052 | 15,503 | 14,767 | 13,435 | 11,655 |
| - Hotel | 4,026 | 3,154 | 3,244 | 2,312 | 1,757 | 1,792 |
| - Industrial | 2,801 | 4,420 | 4,553 | 4,348 | 2,326 | 2,686 |
| - Lighting | 7,127 | 6,409 | 6,202 | 6,110 | 7,054 | 6,566 |
| - Street Lighting | 1,120 | 1,098 | 1,069 | 1,041 | 1,000 | 914 |
| Total | 63,914 | 62,005 | 60,594 | 57,294 | 52,293 | 48,311 |
| Generating Plant kW Installed Capacity |
| - Hydro |  | 7,600 | 7,600 | 7,600 | 7,600 | 7,600 |
| - Diesel |  | 12,840 | 11,090 | 11,090 | 10,036 | 10,036 |
| Total |  | 20,440 | 18,690 | 18,690 | 17,636 | 17,636 |
| Production (kWh X1000) Gross Generation |
| - Hydro | 27,036 | 31,590 | 32,410 | 33,670 | 33,841 | 36,226 |
| - Diesel | 53,929 | 45,336 | 42,226 | 36,630 | 31,942 | 23,867 |
| Total | 80,965 | 76,926 | 74,636 | 70,300 | 65,783 | 60,093 |
| Peak Demand (kW) |
|  | 13866 | 12966 | 13010 | 12348 | 11390 | 10130 |
| Growth (%) | 6.94% | -0.34% | 5.36% | 8.41% | 12.44% |  |
| Source: Dominica Electricity Services Ltd. |

# Footnotes

The Prototype Carbon Fund is an international emissions trading fund, initiated by the World Bank, which sets up a figure on the cost of carbon emissions and encourages companies and institutions to invest in cutting them down.  The fund seeks to invest in green technologies, such as renewable energies; it seeks for restrictions on greenhouse gas emissions and calls for the international trade in emissions.